## Slide 1: Mixture Assessment Factor (MAF): Investigation of the Scientific Basis for its Proposed Application under REACH
John Heinze, Ph.D. Council for LAB/LAS Environmental Research (CLER)

## Slide 2: Mixture Assessment Factor (MAF)
Purpose: To address impacts observed on biota in rivers and streams in Europe
European Commission (EC) proposal as part of the Chemicals Strategy for Sustainability initiative
MAF value to be applied first to registration database of the REACH chemicals program
Current proposal:
  Limited to HPV chemicals (>= 1000 MT/yr), 99% of all tonnage
  MAF value = 5
  Opt-out possible for specific risk assessment + documentation (still to be defined)

## Slide 3: Overview of science
Most recent assessment (UK Government, 2022) reviewed 16 studies on environmental mixtures in the EU and the UK
Conclusions:
Relatively small number of substances responsible for majority of potential risk
  Similar conclusion noted by Vallotton & Price 2016, Posthuma et al 2019, Markert et al. 2020, Van de Meent et al. 2020, Viaene et al. 2021
These substances typically exceed their respective water quality criterion, PNEC or other ecotoxicity threshold
Alternative to MAF: Reduce risk by focusing on those individual chemicals exceeding their ecotoxicity thresholds, ensuring risk management measures are sufficient, before considering mixture risk

## Slide 4: Case Study - LAS
Purpose: Further assess whether a MAF should be applied to ‎all HPV chemicals in the REACH database.
Study substance: linear alkylbenzene sulfonate (LAS)
LAS is arguably the best available case study‎
More environmental mixture data than any other down-the-drain disposal ‎chemical
  Additivity studies (2)
  Eco-epidemiology studies (7) ‎

## Slide 5: Additivity studies
Focus: components of environmental mixtures having same/similar mode of action (MoA)
Procedure:
  Calculate toxicity fraction for each chemical species present:
  MEC/PNEC
  Add fractional toxicity to determine toxicity of mixture
Scope: Additivity studies conducted with anionic and nonionic surfactants (MoA = narcosis)

## Slide 6: LAS Additivity Study (1)
McDonough et al. (2016) – Probabilistic assessment of US freshwater, focusing on WWTP receiving waters
  Used monitoring data for LAS, alcohol sulfates (AS), alcohol ethoxysulfates (AES) and ‎methyl ester sulfonates in WWTP effluents
  Modeled mixing zone concentrations for 8,800 sites throughout the U.S. (‎iSTREEM® flow model)
  The 90th percentile toxic ‎unit value (0.0421) at critical low flow (CLF) demonstrated large margin of safety (>20 fold)
    CLF = seven lowest consecutive flow days over a 10-year period

## Slide 7: LAS Additivity Study (2)
‎Freeling et al. 2019 – Monitoring study of receiving water mixing ‎zones from 33 WWTPs in Germany
Measured concentrations of anionic and nonionic surfactants, including LAS, AS, ‎AES and alkyl ethoxylates, their byproducts and degradation products
Cumulative risk ratios were less than 1.0 for all WWTPs except one where the ‎calculated cumulative risk ratio was 1.06
However, LAS REACH PNEC value not used; reanalysis using REACH value indicates all 33 sites had cumulative risk ratios less ‎than 1.0 (Dyer & Belanger 2020)

## Slide 8: Eco-epidemiology studies
These compare the biological status (health) of environmental compartments with environmental stressors, looking for correlations
Stressors can include individual chemicals or mixtures as well as stream habitat loss, urban vs agricultural runoff, etc.
Mixtures can include all chemicals present, regardless of MoA

## Slide 9: LAS Eco-epidemiology studies (1)
Study | Sites | Effects Measured | Conclusion
Dyer and Wang 2002 | Urban and rural sites upstream and downstream of 221 WWTPs in Ohio, USA | Fish and macroinvertebrate communities | No impacts linked to effluents >> no impact from effluent components, including LAS
Sanderson et al. 2006 | LAS, AES and AE upstream and downstream of 3 rural WWTPs in Indiana and Ohio, USA | Macroinvertebrate richness and abundance | No statistically significant adverse relationships

## Slide 10: LAS Eco-epidemiology studies (2)
Study | Sites | Effects Measured | Conclusion
De Zwart et al. 2006 | Modeled concentrations of LAS and 10 other down-the-drain chemicals at 695 sites in Ohio, USA | Loss of fish species | 3% of observed impacts linked to mixture concentrations
Atkinson et al. 2009 and Slye et al. 2011 | LAS, other surfactants, water quality, habitat and WWTPs in effluent dominated Trinity River, Texas, USA | Benthic macroinvertebrate community structure | Total surfactant toxic units low, no correlation with any benthic variable.

## Slide 11: LAS Eco-epidemiology studies (3)
Study | Sites | Effects Measured | Conclusion
Kapo et al. (2014) | Chemical mixtures, habitat, watershed, soils, population, WWTPs, and landcover at 1700 sites in Ohio, USA | Fish and macroinvertebrate communities | LAS and 6 other household product ingredients were not a major factor for adverse effects
Holmes et al. 2021a,b | Surfactant (LAS) concentration at 3970 river and stream sites in Federal state of Hessen in Germany | Biological Quality Elements (BQEs) for fish, macro-invertebrates, diatoms and macrophytes | LAS did not drive ecological status

## Slide 12: LAS Eco-epidemiology studies (4)
Study | Sites | Effects Measured | Conclusion
Dyer et al. 2003 | LAS, water quality parameters along Balatuin River, Philippines, upstream and downstream of urban site with multiple primary sewage discharges | Changes in water quality parameters (highly impacted river with limited aquatic ecology) | LAS concentrations were below protective criteria even in impact zone with high BOD, low dissolved oxygen and high ammonia nitrogen

## Slide 13: Conclusions
LAS mixture studies do not support the EC proposal to apply MAF=5 to all HPV chemicals in the REACH registration database
  Strengths: best case study based on available environmental mixture data
  Limitations: one chemical study, only relevant to down-the-drain chemicals
LAS data support alternative proposal (from multiple authors) that improvements in environmental protection should focus on those few chemicals with environmental impacts
Suggested path forward:
  Reduce risk by focusing on individual chemicals observed exceeding their respective ecotoxicity thresholds
  Further research on optimal application of MAF

## Slide 14: References
Full text, including references and supporting studies, available in The CLER Review, vol. 18, available at:
https://cler.com/the-cler-review/

## Slide 15: Thank you